# RJ45 bulhead set T568B metal IP68 outdoor

Bulkhead set TOC system suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. RJ45 module cat.6A,

operating temperature -40°C to +85°C,

ROHS compliant

RJ45 module:

- Category 6A

- suitable for 10 Gigabit Ethernet

- approved for RJ11/12/45 plugs

- robust housing made of die-cast

- Insertion life:    min. 750 mating cycles

- Wire connection:   IDC

- Conductor:         AWG26/1 to AWG22/1;

AWG26/7 to AWG22/7

- Cable diameter:    5.5mm to 10.0mm

- Pin/pair assignment: T568B

- bonding connection 2.8mm DIN 46342-1

- integrated cable strain relief

- separate integrated shield contact

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Mounting cut-out: Round hole, diam. 30.5mm

- Mounting:         4 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC bulkhead set IP68

AMJ-S module T568B Cat6A

Part no.:           100007379