# RJ45 bulkhead set coupler metal IP68 outdoor

Bulkhead set TOC system suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. RJ45 coupler cat.6/class EA,

operating temperature -40°C to +85°C,

ROHS compliant

RJ45 coupler:

- Category 6

- Link class EA

- suitable for 10 Gigabit Ethernet

- approved for RJ11/12/45 plugs

- robust housing made of die-cast

- Insertion life:    min. 750 mating cycles

- advanced resistance to vibrations and shock

due to four elastic shield mating areas

- bonding connection 2.8mm DIN 46342-1

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Mounting cut-out: Round hole, diam. 30.5mm

- Mounting:         4 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC bulkhead set IP68

AMJ coupler K Cat6

Part no.:           100007381