# RJ45 coupler metal IP68 outdoor

Coupler TOC system with connection for TOC plug on both sides, suitable for industrial applications,

for flexible link expansion of generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. screws to attach two bulkhead protection caps IP68,

incl. RJ45 coupler cat.6/class EA,

operating temperature -40°C to +85°C,

ROHS compliant

RJ45 coupler:

- Category 6

- Link class EA

- suitable for 10 Gigabit Ethernet

- approved for RJ11/12/45 plugs

- robust housing made of die-cast

- Insertion life:    min. 750 mating cycles

- advanced resistance to vibrations and shock

due to four elastic shield mating areas

- bonding connection 2.8mm DIN 46342-1

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Outer diameter:   40.0mm

- Length:           45.0 mm

- Mounting:         2 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC coupler IP68

AMJ coupler K

Part no.:           100007390