# LC/APC-D SM plug set metal IP68 outdoor

Plug set TOC system suitable for industrial applications,

for generic cabling,

for cable diameters 4mm to 9 mm,

suitable for permanent outdoor use,

incl. LC/APC duplex plug

for singlemode fibers

operating temperature -40°C to +85°C,

ROHS compliant

LC/APC duplex plug:

- Standard:         IEC 61754-20

- Ferrule:          ceramic

- Insertion life:   min. 1000 mating cycles

- Tensile strength: min. 100N

- Insertion loss:   max. 0.5dB

- IL change:        max. 0.2dB

after 500 mating cycles

- Return loss:      factory assembled

min. 60dB

- Housing:          flame retardant zero halogen

- Colour:           green

- Boot:             flame retardant zero halogen

elastomere

- Dust cap:         flame retardant zero halogen

elastomere

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

Manufacturer:       Telegärtner

Type:               TOC plug set IP68 LC/APC

duplex SM metal

Part no.:           100007395