# LC-D SM/MM bulkhead set metal IP68 outdoor

Bulkhead set TOC system suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. LC duplex adaptor

for singlemode and multimode fibers

operating temperature -40°C to +85°C,

ROHS compliant

LC duplex adaptor:

- Standard:         IEC 61754-20

- Sleeve:           ceramic, slottet

- Housing:          PBT UL94 V, flame retardant,

zero halogen

- Colour:           blue

- Dust cap:         flame retardant zero halogen

elastomere

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Mounting cut-out: Round hole, diam. 30.5mm

- Mounting:         4 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC bulkhead set IP68 LC

duplex SM MM metal

Part no.:           100007403