# LC/APC-D bulkhead set metal IP68 outdoor

Bulkhead set TOC system suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. LC/APC duplex adaptor

operating temperature -40°C to +85°C,

ROHS compliant

LC/APC duplex adaptor:

- Standard:         IEC 61754-20

- Sleeve:           ceramic, slottet

- Housing:          PBT UL94 V, flame retardant,

zero halogen

- Colour:           green

- Dust cap:         flame retardant zero halogen

elastomere

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Mounting cut-out: Round hole, diam. 30.5mm

- Mounting:         4 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC bulkhead set IP68 LC

duplex SM APC metal

Part no.:           100007404