# LC-D SM/MM coupler metal IP68 outdoor

Coupler TOC system with connection for TOC plug on both sides, suitable for industrial applications,

for flexible link expansion of generic cabling,

suitable for permanent outdoor use,

round mounting hole,

incl. screws to attach two bulkhead protection caps IP68,

incl. LC duplex adaptor

for singlemode and multimode fibers

operating temperature -40°C to +85°C,

ROHS compliant

LC duplex adaptor:

- Standard:         IEC 61754-20

- Sleeve:           ceramic, slottet

- Housing:          PBT UL94 V, flame retardant,

zero halogen

- Colour:           blue

- Dust cap:         flame retardant zero halogen

elastomere

Housing

- Housing type:     TOC

- Mating:           screw coupling with

multiple sealings

- IP rating:        IP68

- Material:         nickel-plated brass

- Outer diameter:   40.0mm

- Length:           45.0 mm

- Mounting:         2 x screw (M3)

Manufacturer:       Telegärtner

Type:               TOC coupler IP68 LC

duplex SM MM metal

Part no.:           100007407