# Mounting bracket for TOC bulkhead outlets

Mounting bracket for TOC system, suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

for wall mount, ceiling mount and DIN rail mount (TH35),

operating temperature -40°C to +85°C

Material: stainless steel

Thickness: 2.0mm

Stub 1:

- Length: 50mm

- Width: 45mm

- 5 holes of 4.32mm, cross-pattern

- 4 holes of 3.4 mm, rectangular pattern

Stub 2:

- Length: 53mm

- Width: 45mm

- 1 hole of 34.4mm accepts TOC bulkhead outlet

- 4 holes of 4.3 mm, rectangular pattern

Agle of 80 degress between stubs

Comes with two mounting rail adaptors made of spring steel for DIN rail mount (TH35), incl. six screws M4x8 made of stainless steel

Manufacturer:       Telegärtner

Type:               TOC mounting bracket

gauge 38 mm and TH35

Part no.:           100022656