# Pole mounting bracket for TOC bulkhead outlet

Mounting bracket for TOC system, suitable for industrial applications,

for generic cabling,

suitable for permanent outdoor use,

for mounting on poles using sign holders,

operating temperature -40°C to +85°C

Material: stainless steel

Thickness: 2.0mm

Stub 1:

- Length: 40mm

- Width: 55mm

- 2 holes of 8.8mm, distance 37.5 mm

for mounting on sign holder

Stub 2:

- Length: 63mm

- Width: 55mm

- 1 hole of 34.4mm accepts TOC bulkhead outlet

- 4 holes of 4.3mm, rectangular pattern

Angle of 90 degrees between stubs

Incl. four screws M4x8 made of stainless steel

Manufacturer:       Telegärtner

Type:               TOC mounting bracket

gauge 37.5mm for

sign holder

Part no.:           100022656