# 19“ FO patch panel 1HU, 12xSC-D, OM3, Basis

accepts up to 2 splice cassetts for up to 24 splices each;

splice cassettes have integrated splice holders;

cover on top splice cassette;

Minimum of 4 cable entries on the rear, cables can be layed into opening from above;

base has a minimum of 6 mounting brackets for cable ties or hook-and-loop strips;

removable, end-to-end front plate with 12 pre-installed SC duplex adaptors;

adaptors bolted in place;

pigtails stripped ready to be spliced and routed in splice cassette(s);

plugs of pigtails plugged in the adaptors;

pigtails in 12 different colours according to IEC 60304;

dust protection plugged into adaptors (at the outside);

Features:

Depth:            max. 251mm

Cable diameters:  5...20mm possible

Materials:

Housing:      sheet steel, powder coated

Front plate:  aluminium, powder coated

Colour:       light grey like RAL 7035

Pigtail:

- Fiber type:         IEC 60793-2-10 / OM3

- Secondary coating:  max. 900µm, coloured

- Crush resistance:   min. 1000N/m

- Insertion loss:     max. 1.0dB/km at 1300nm

- Plug:               SC acc. to IEC61754-4

- Mating cycles:      min. 1000

- Ferrule:            zirconia ceramic

- RL:                 min. 30dB

SC duplex adaptor:

- Standard:  IEC 61754-4

- Sleeve:    zirconia ceramic, slotted

- Housing:   halogen-free plastic;

- Colour:    aqua

- Dust protection

1 of M20 cable gland, 1 of M25 cable gland and 2 of blanks included

Manufacturer:   Telegärtner

Type:           BASIS eco

Part No.:       H02030K9009