# 19“ FO patch panel 1HU, 12xLC-D, OM4, Economy

for the connection of pre-terminated cables;

recessed mounting of up to 50mm possible;

cable strain relief bar on the rear with latches for cable ties or hook-and-loop strips;

removable front plate with 12 pre-installed LC duplex adaptors;

adaptors bolted in place;

dust protection plugged into adaptors (at the outside);

Features:

Depth:            max. 175mm

Materials:

Housing:      sheet steel, powder coated

Front plate:  aluminium, powder coated

Colour:       light grey like RAL 7035

LC duplex adaptor:

- Standard:  IEC 61754-20

- Sleeve:    zirconia ceramic, slotted

- Housing:   halogen-free plastic;

- Colour:    violet

- Dust protection

Manufacturer:   Telegärtner

Type:           Economy V

Part No.:       H02030N0609